## Slide 1: Stinson L-5 (Sentinel)
Miss Ziggy
STANDARD DATA:
Seats 2.
Gross wt. 2050.
Fuel capacity 36 gallons.
Engine 190-hp Lycoming.
PERFORMANCE:
Top mph 130.
Cruise mph 112.
Initial climb rate 975.
Ceiling 15,800.
Range 275.
Maximum range 420.
1
Single Engine Ground

## Slide 2: Stinson L-5
Sentinel
Between December 1942 and September 1945 3,590 L-5's were built.
It's primary purpose as a liaison aircraft was courier and communication work, artillery spotting and casualty evacuation.
2
Single Engine Ground

## Slide 3: Stinson L-5
Takeoff speeds
Flaps Down 51 mph
Flaps Up 57 mph
Takeoff Power
2250, 5 minute max.
Normal Cruise
2200 rpm
Flap Settings ………300 and 450
Stall Speeds
Power OFF Flaps Up…….. 57
Power OFF Flaps Down.… 49
Max Dive Speed……………… 208
Best Glide Speed…………….…70
3
Single Engine Ground
Limitations

## Slide 4: Stinson L-5
Maximum Flap Operating Speed……..100 mph
Electrical system is…………………….…. 12 VDC
Minimum and maximum oil…………… 6 / 12 quarts
Maximum Gross Weight………………. 2050 pounds
Maximum Crew Weight……………….. 400 pounds
4
Single Engine Ground
Limitations

## Slide 5: Stinson L-5
Hardy main gear allows operation from unimproved fields.
Note: Main gear has significant travel. This can result in interesting ground handling if the lateral axis is not aligned.
5
Single Engine Ground
Landing Gear

## Slide 6: Stinson L-5
Airspeed
Altimeter
Ampmeter
Clock
Compass
Oil Pressure
Oil Temperature
Tachometer
6
Single Engine Ground
Instruments

## Slide 7: Stinson L-5
Main gear and tail struts allows operation from unimproved fields.
7
Single Engine Ground
Landing Gear

## Slide 8: Stinson L-5
8
Single Engine Ground
Landing Gear
Struts are oleo. Which means they must be properly serviced to function correctly.

## Slide 9: Stinson L-5
The master switch / breaker is located behind the pilots right shoulder.
9
Single Engine Ground
Master Switch
Generator and battery switches are on the panel on the upper left.

## Slide 10: Stinson L-5
Elevator trim is controlled from the front seat with the trim crank on the left side.
From the rear seat, adjustments can be made by grasping and pulling the trim wires.
10
Single Engine Ground
Trim
Rudder trim is not adjustable from inside the aircraft.

## Slide 11: Stinson L-5
Fuel capacity is 36 gallons. 18 gallons in each wing tank.
11
Single Engine Ground
Fuel
Fuel is gravity feed. Tank selection is via the tank selection switch. Selections are Left, Right, Both Off, Both Off.
Simultaneously feeding from
both tanks is not available.
Fuel quantity gauges are located near the wing spars.

## Slide 12: Stinson L-5
Fuel Feed
12
Single Engine Ground
Fuel is fed from the tanks to the fuel selector via tubing which angles through the cockpit.
The one on the right is often mistaken for a part of the aircraft structural tubing. It is not! And should not be used as a hand hold.

## Slide 13: Stinson L-5
Tail Wheel
13
Single Engine Ground
The L-5 is equipped with a steerable tailwheel. The wheel will become free-castering when sufficient pressure is put on the locking pin to force it out of the detent.

## Slide 14: Stinson L-5
14
Single Engine Ground
What is the fuel capacity?
What is the reserve fuel? Which tank?
What is the maximum flap extension speed?
What are the flap settings?
Which parking brake setting is OFF?
36 gallons
Trick question… None
100 MPH
30º, 45º
Right
System / Performance Questions

## Slide 15: Stinson L-5
15
Single Engine Ground
What speed is Best Glide?
What the maximum crosswind speed?
What voltage is the electrical system?
What is the minimum oil?
Maximum gross weight is? Max crew weight?
70 mph
~15 knots, not published
12 VDC
6 quarts
2050 / 400
System / Performance Questions